## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Electrical Safety for Non-Qualified Employees
Professional downloadable safety training
TRAINING OUTCOME
Recognize common electrical hazards and damaged equipment
AUDIENCE
Employees who may face electrical hazards
TIME
30-40 min
REFERENCE
29 CFR 1910.332 / 1910 Subpart S
USE NOTE
Awareness for non-qualified employees. Only qualified persons may perform work that requires the knowledge/skills and permissions assigned to qualified electrical workers.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Electrical Safety for Non-Qualified Employees to the actual work employees perform. Awareness for non-qualified employees. Only qualified persons may perform work that requires the knowledge/skills and permissions assigned to qualified electrical workers.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Know your role
Non-qualified employees need safety practices necessary for their work but are not authorized to perform qualified electrical tasks.
Cords, plugs and tools
Inspect for cut insulation, missing ground pins, damaged strain relief, exposed conductors and heat damage.
Panels and access
Keep electrical equipment access clear.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize common electrical hazards and damaged equipment
02
Distinguish non-qualified versus qualified work boundaries
03
Use cords, plugs and portable equipment safely
04
Respond safely to shock, fire, wet conditions and exposed energized parts
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Know your role
Start with what the employee is exposed to.
Non-qualified employees need safety practices necessary for their work but are not authorized to perform qualified electrical tasks.
Do not open panels, defeat interlocks or work on exposed energized parts unless specifically qualified/authorized.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Know your role,Non-qualified employees need safety practices necessary for their work but are not authorized to perform qualified electrical tasks.,Do not open panels, defeat interlocks or work on exposed energized parts unless specifically qualified/authorized.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Cords, plugs and tools
Tie every point to a visible action or decision.
Inspect for cut insulation, missing ground pins, damaged strain relief, exposed conductors and heat damage.
Remove defective equipment from service.
Use equipment rated for the environment and follow GFCI/assured grounding requirements where applicable.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Cords, plugs and tools,Inspect for cut insulation, missing ground pins, damaged strain relief, exposed conductors and heat damage.,Remove defective equipment from service.,Use equipment rated for the environment and follow GFCI/assured grounding requirements where applicable.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Panels and access
Tie every point to a visible action or decision.
Keep electrical equipment access clear.
Do not store materials in required working space.
Report open covers, missing blanks, damaged enclosures or signs of overheating.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Panels and access,Keep electrical equipment access clear.,Do not store materials in required working space.,Report open covers, missing blanks, damaged enclosures or signs of overheating.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Wet locations and grounding
Tie every point to a visible action or decision.
Water increases shock risk.
Use approved equipment/protection for wet/damp locations.
Never improvise adapters or defeat grounding.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Wet locations and grounding,Water increases shock risk.,Use approved equipment/protection for wet/damp locations.,Never improvise adapters or defeat grounding.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Overhead and exposed parts
Tie every point to a visible action or decision.
Maintain required clearance from overhead/exposed energized parts based on employer procedure and applicable standard.
Use barriers/qualified assistance when work could encroach.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Overhead and exposed parts,Maintain required clearance from overhead/exposed energized parts based on employer procedure and applicable standard.,Use barriers/qualified assistance when work could encroach.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Emergency response
Tie every point to a visible action or decision.
Do not touch a person who is still in contact with electricity until the source is safely controlled.
Call emergency response and use trained rescue/first-aid procedures.
Electrical fires may require specific extinguisher selection and de-energization.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Emergency response,Do not touch a person who is still in contact with electricity until the source is safely controlled.,Call emergency response and use trained rescue/first-aid procedures.,Electrical fires may require specific extinguisher selection and de-energization.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Damaged cord/plug or missing ground pin
02
Open electrical panel or exposed live parts
03
Wet work near non-rated electrical equipment
04
Employee preparing to reset/work inside equipment beyond their qualification
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A worker finds an extension cord with a cut jacket and visible conductor but says it only powers a small fan. What should happen?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Remove the cord from service immediately and replace/repair it through an approved process; load size does not make exposed conductors safe.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Remove the cord from service immediately and replace/repair it through an approved process; load size does not make exposed conductors safe.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Define what non-qualified employees may and may not do
✓
Show defect tagging/removal process
✓
Review GFCI/wet-location rules and extension-cord policy
✓
Identify restricted electrical areas and emergency response
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Inspects cord/tool
Identifies panel clearance problem
Explains non-qualified boundary
Reports damaged equipment
Uses GFCI/site protection correctly
Describes electrical emergency action
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
A non-qualified employee should:
2
A cord with exposed conductor should be:
3
Electrical panel working space should be:
4
A missing grounding pin is:
5
Wet conditions generally:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
If a person is in contact with energized equipment, a rescuer should:
7
Qualified electrical work requires:
8
Overhead electrical hazards require:
9
Defective electrical equipment should be:
10
This awareness course makes someone a qualified electrical person.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize common electrical hazards and damaged equipment
02
Damaged cord/plug or missing ground pin
03
Define what non-qualified employees may and may not do
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.332 / 1910 Subpart S
Training use note
Awareness for non-qualified employees. Only qualified persons may perform work that requires the knowledge/skills and permissions assigned to qualified electrical workers.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/laws-regs/regulations/standardnumber/1910/1910.332
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.