## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Powered Industrial Trucks / Forklift Fundamentals
Professional downloadable safety training
TRAINING OUTCOME
Explain forklift stability, load center and center-of-gravity basics
AUDIENCE
Forklift / PIT operators
TIME
40-55 min
REFERENCE
29 CFR 1910.178(l)
USE NOTE
Formal instruction component only. Practical training and workplace evaluation by a qualified trainer are required before independent operation.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Powered Industrial Trucks / Forklift Fundamentals to the actual work employees perform. Formal instruction component only. Practical training and workplace evaluation by a qualified trainer are required before independent operation.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Forklifts are not cars
Rear-wheel steering changes how the back end swings.
Pre-use inspection
Inspect tires, forks, mast, chains, hydraulics, controls, horn, brakes, lights and safety devices as applicable.
Load handling
Know capacity plate limits and attachments.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Explain forklift stability, load center and center-of-gravity basics
02
Use safe travel, visibility, pedestrian and dock practices
03
Recognize truck-specific and workplace-specific hazards
04
Understand OSHA requirements for practical training, evaluation, refresher training and certification
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Forklifts are not cars
Start with what the employee is exposed to.
Rear-wheel steering changes how the back end swings.
A high center of gravity and narrow stability triangle make tip-over possible.
Loads change steering, braking, visibility and stability.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Forklifts are not cars,Rear-wheel steering changes how the back end swings.,A high center of gravity and narrow stability triangle make tip-over possible.,Loads change steering, braking, visibility and stability.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Pre-use inspection
Tie every point to a visible action or decision.
Inspect tires, forks, mast, chains, hydraulics, controls, horn, brakes, lights and safety devices as applicable.
Remove unsafe trucks from service.
Know battery/LP/fuel hazards and charging/refueling rules.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Pre-use inspection,Inspect tires, forks, mast, chains, hydraulics, controls, horn, brakes, lights and safety devices as applicable.,Remove unsafe trucks from service.,Know battery/LP/fuel hazards and charging/refueling rules.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Load handling
Tie every point to a visible action or decision.
Know capacity plate limits and attachments.
Center and secure the load; tilt only as needed.
Travel with the load low enough for stability and visibility.
Never raise or transport people on forks unless using an approved personnel platform and procedure.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Load handling,Know capacity plate limits and attachments.,Center and secure the load; tilt only as needed.,Travel with the load low enough for stability and visibility.,Never raise or transport people on forks unless using an approved personnel platform and procedure.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Travel and visibility
Tie every point to a visible action or decision.
Look in the direction of travel; travel in reverse when the load blocks the view unless site rules specify another safe method.
Slow at intersections, blind corners and wet/uneven surfaces.
Maintain clearances from edges, racks, doorways and overhead hazards.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Travel and visibility,Look in the direction of travel; travel in reverse when the load blocks the view unless site rules specify another safe method.,Slow at intersections, blind corners and wet/uneven surfaces.,Maintain clearances from edges, racks, doorways and overhead hazards.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Pedestrians, docks and trailers
Tie every point to a visible action or decision.
Separate pedestrian routes where feasible.
Sound the horn at cross aisles and obstructed locations per site rules.
Verify dock plates, trailer restraint/chocks and floor capacity before entry.
Never allow people under elevated forks or loads.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Pedestrians, docks and trailers,Separate pedestrian routes where feasible.,Sound the horn at cross aisles and obstructed locations per site rules.,Verify dock plates, trailer restraint/chocks and floor capacity before entry.,Never allow people under elevated forks or loads.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Training and evaluation
Tie every point to a visible action or decision.
Formal instruction must be combined with practical training and workplace evaluation.
Operators need refresher training after unsafe operation, an accident/near miss, unsafe evaluation, different truck assignment, or workplace change.
Operator performance must be evaluated at least once every three years.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Training and evaluation,Formal instruction must be combined with practical training and workplace evaluation.,Operators need refresher training after unsafe operation, an accident/near miss, unsafe evaluation, different truck assignment, or workplace change.,Operator performance must be evaluated at least once every three years.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Capacity plate is unreadable or attachment changes capacity
02
Load blocks view and operator continues forward blindly
03
Pedestrian enters the truck path without eye contact or separation
04
Truck has brake, steering, fork, tire or hydraulic defects
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A loaded forklift is approaching a blind intersection while a pedestrian is walking in the cross aisle. What should the operator do?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Slow or stop as needed, sound the horn per site rules, maintain control and proceed only after the path is clear and pedestrian separation is established.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Slow or stop as needed, sound the horn per site rules, maintain control and proceed only after the path is clear and pedestrian separation is established.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Train on each truck type actually used and manufacturer instructions
✓
Review traffic routes, pedestrian controls, ramps, docks, trailers and hazardous areas
✓
Conduct hands-on practice under qualified supervision
✓
Evaluate the operator in the actual workplace and document training/evaluation
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Completes pre-use inspection
Uses seat belt/restraint when provided
Maintains low stable travel position
Uses safe speed and controlled turns
Demonstrates safe load pickup/placement
Maintains pedestrian separation and horn use
Safely approaches docks/ramps/trailers
Parks truck with forks lowered and controls neutralized
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
OSHA PIT training must include:
2
Operator performance must be evaluated at least:
3
A forklift load should generally be carried:
4
If a load blocks forward view, the operator should:
5
Pedestrians should:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
A truck with a safety defect should be:
7
Refresher training can be triggered by:
8
The capacity plate matters because it:
9
At a blind intersection the operator should:
10
Passing this course by itself means the employee is OSHA-certified to operate a forklift.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Explain forklift stability, load center and center-of-gravity basics
02
Capacity plate is unreadable or attachment changes capacity
03
Train on each truck type actually used and manufacturer instructions
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.178(l)
Training use note
Formal instruction component only. Practical training and workplace evaluation by a qualified trainer are required before independent operation.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/etools/powered-industrial-trucks/training
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.