## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Front-End Loader Safety Fundamentals
Professional downloadable safety training
TRAINING OUTCOME
Recognize rollover, struck-by, blind-spot and load hazards
AUDIENCE
Loader operators & spotters
TIME
30-40 min
REFERENCE
29 CFR 1926.602 / applicable ROPS requirements + manufacturer instructions
USE NOTE
General formal instruction. Employer must provide model-specific hands-on training, manufacturer requirements and task/worksite evaluation.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Front-End Loader Safety Fundamentals to the actual work employees perform. General formal instruction. Employer must provide model-specific hands-on training, manufacturer requirements and task/worksite evaluation.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Machine stability
Bucket/load changes the center of gravity.
Pre-use inspection
Check tires/tracks, steering, brakes, hydraulics, bucket/attachment, pins, lights, horn/back-up alarm/camera and safety devices.
Visibility and people
Large blind areas exist around loaders.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize rollover, struck-by, blind-spot and load hazards
02
Inspect loader, attachment and work area before use
03
Travel, load, dump and park with stable bucket position and controlled speed
04
Coordinate safely with spotters, pedestrians, trucks and slopes
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Machine stability
Start with what the employee is exposed to.
Bucket/load changes the center of gravity.
Slopes, uneven ground, sharp turns, raised loads and speed increase rollover risk.
Use ROPS and seat belt/restraint as equipped and required.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Machine stability,Bucket/load changes the center of gravity.,Slopes, uneven ground, sharp turns, raised loads and speed increase rollover risk.,Use ROPS and seat belt/restraint as equipped and required.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Pre-use inspection
Tie every point to a visible action or decision.
Check tires/tracks, steering, brakes, hydraulics, bucket/attachment, pins, lights, horn/back-up alarm/camera and safety devices.
Walk the area for drop-offs, soft ground, overhead lines and traffic.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Pre-use inspection,Check tires/tracks, steering, brakes, hydraulics, bucket/attachment, pins, lights, horn/back-up alarm/camera and safety devices.,Walk the area for drop-offs, soft ground, overhead lines and traffic.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Visibility and people
Tie every point to a visible action or decision.
Large blind areas exist around loaders.
Use cameras/mirrors as aids, not substitutes for looking and site controls.
Use a trained spotter when required and establish clear signals.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Visibility and people,Large blind areas exist around loaders.,Use cameras/mirrors as aids, not substitutes for looking and site controls.,Use a trained spotter when required and establish clear signals.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Travel and load position
Tie every point to a visible action or decision.
Carry the bucket/load low for stability and visibility.
Avoid sudden turns/braking and travel at a speed suitable for ground conditions.
Do not travel with people in the bucket.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Travel and load position,Carry the bucket/load low for stability and visibility.,Avoid sudden turns/braking and travel at a speed suitable for ground conditions.,Do not travel with people in the bucket.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Loading and dumping
Tie every point to a visible action or decision.
Approach piles/trucks squarely and maintain stable ground.
Do not undercut unstable material or work below unsupported loads.
Keep people clear of bucket swing/dump zones.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Loading and dumping,Approach piles/trucks squarely and maintain stable ground.,Do not undercut unstable material or work below unsupported loads.,Keep people clear of bucket swing/dump zones.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Slopes, parking and maintenance
Tie every point to a visible action or decision.
Follow manufacturer slope limits and travel orientation.
Park on stable ground, lower attachment, neutralize controls, set brake and shut down.
Block/support raised components before maintenance; never rely only on hydraulics.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Slopes, parking and maintenance,Follow manufacturer slope limits and travel orientation.,Park on stable ground, lower attachment, neutralize controls, set brake and shut down.,Block/support raised components before maintenance; never rely only on hydraulics.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Traveling with bucket high
02
Person enters blind spot without positive communication
03
Working near edge/soft ground or excessive slope
04
Maintenance under a raised bucket without approved blocking/support
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A loader operator needs to drive across uneven ground with a full bucket. What bucket position is generally safest?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Carry the load as low as practical while maintaining safe ground clearance, use controlled speed and follow the manufacturer/site procedure.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Carry the load as low as practical while maintaining safe ground clearance, use controlled speed and follow the manufacturer/site procedure.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Actual loader controls, attachment and manufacturer manual
✓
Site traffic plan, spotter signals and backing controls
✓
Slope/edge/ground conditions and overhead clearances
✓
Hands-on loading/dumping and workplace evaluation
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Performs walk-around/pre-use inspection
Uses seat belt/restraint
Checks blind areas and work zone
Maintains low travel load
Controls speed/turns
Coordinates with spotter
Loads/dumps without exposing people
Parks/lowers attachment safely
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
A raised loader bucket generally:
2
A loader operator should normally travel with the bucket:
3
Blind spots are best controlled with:
4
Before operating, inspect:
5
On slopes the operator should:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
People should be:
7
Maintenance under a raised attachment requires:
8
ROPS and operator restraint:
9
A spotter should use:
10
This course alone qualifies an operator on every loader model.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize rollover, struck-by, blind-spot and load hazards
02
Traveling with bucket high
03
Actual loader controls, attachment and manufacturer manual
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1926.602 / applicable ROPS requirements + manufacturer instructions
Training use note
General formal instruction. Employer must provide model-specific hands-on training, manufacturer requirements and task/worksite evaluation.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926.602
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.