## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Lockout / Tagout (LOTO)
Professional downloadable safety training
TRAINING OUTCOME
Recognize hazardous energy sources and when LOTO applies
AUDIENCE
Authorized & affected employees
TIME
35-45 min
REFERENCE
29 CFR 1910.147
USE NOTE
General/formal instruction. Employer- and machine-specific energy-control procedures are still required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Lockout / Tagout (LOTO) to the actual work employees perform. General/formal instruction. Employer- and machine-specific energy-control procedures are still required.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
When LOTO applies
Servicing or maintenance can expose workers to unexpected startup, movement, pressure, gravity, heat or stored energy.
Roles and responsibilities
Authorized employees apply and control locks/tags for servicing work.
The energy-control sequence
Prepare for shutdown and identify every energy source.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize hazardous energy sources and when LOTO applies
02
Explain authorized, affected and other employee roles
03
Follow the basic sequence for shutdown, isolation, lock/tag, stored-energy control and verification
04
Recognize group, shift-change and contractor situations that need special control
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
When LOTO applies
Start with what the employee is exposed to.
Servicing or maintenance can expose workers to unexpected startup, movement, pressure, gravity, heat or stored energy.
A normal stop button is not an energy-isolating device.
Production work can become covered when guards are bypassed or a body part enters a danger zone.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - When LOTO applies,Servicing or maintenance can expose workers to unexpected startup, movement, pressure, gravity, heat or stored energy.,A normal stop button is not an energy-isolating device.,Production work can become covered when guards are bypassed or a body part enters a danger zone.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Roles and responsibilities
Tie every point to a visible action or decision.
Authorized employees apply and control locks/tags for servicing work.
Affected employees operate/use the equipment or work in the area and must understand the purpose of the procedure.
Other employees must know not to restart or interfere with locked/tagged equipment.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Roles and responsibilities,Authorized employees apply and control locks/tags for servicing work.,Affected employees operate/use the equipment or work in the area and must understand the purpose of the procedure.,Other employees must know not to restart or interfere with locked/tagged equipment.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
The energy-control sequence
Tie every point to a visible action or decision.
Prepare for shutdown and identify every energy source.
Notify affected employees, stop the machine, isolate energy sources and apply locks/tags.
Release, block or restrain stored energy.
Verify isolation before work begins.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - The energy-control sequence,Prepare for shutdown and identify every energy source.,Notify affected employees, stop the machine, isolate energy sources and apply locks/tags.,Release, block or restrain stored energy.,Verify isolation before work begins.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Verification is a step, not a feeling
Tie every point to a visible action or decision.
Try-start or other approved verification must confirm the isolation is effective.
Testing must be performed using the employer procedure and appropriate instruments where needed.
Re-verify when conditions change or energy could reaccumulate.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Verification is a step, not a feeling,Try-start or other approved verification must confirm the isolation is effective.,Testing must be performed using the employer procedure and appropriate instruments where needed.,Re-verify when conditions change or energy could reaccumulate.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Group work and shift changes
Tie every point to a visible action or decision.
Each exposed authorized employee needs equivalent personal protection.
Shift changes must maintain continuity of protection.
Contractors and host employers must exchange LOTO procedure information.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Group work and shift changes,Each exposed authorized employee needs equivalent personal protection.,Shift changes must maintain continuity of protection.,Contractors and host employers must exchange LOTO procedure information.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Safe return to service
Tie every point to a visible action or decision.
Inspect the work area, replace guards and remove tools.
Confirm employees are clear and account for personnel.
Locks/tags are normally removed by the employee who applied them, except under a documented employer procedure.
Notify affected employees before returning equipment to service.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Safe return to service,Inspect the work area, replace guards and remove tools.,Confirm employees are clear and account for personnel.,Locks/tags are normally removed by the employee who applied them, except under a documented employer procedure.,Notify affected employees before returning equipment to service.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Someone says “it is off” but cannot identify all energy sources
02
A lock is missing a name/identity
03
Stored pressure, gravity or heat has not been controlled
04
Someone wants to remove another employee’s lock without the employer procedure
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A mechanic locks out electrical power to a conveyor but does not block the raised pneumatic gate. The gate can fall if pressure bleeds off. What is missing?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Stored energy must be relieved, restrained or otherwise rendered safe before work begins.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Stored energy must be relieved, restrained or otherwise rendered safe before work begins.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Show the written energy-control program and machine-specific procedures
✓
Identify actual isolation points and stored-energy hazards
✓
Demonstrate employer locks/tags and verification method
✓
Explain group LOTO, contractor coordination, shift change and emergency lock-removal rules
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Identifies all energy sources before shutdown
Selects correct isolation devices
Applies personal lock/tag correctly
Controls stored or residual energy
Performs approved verification step
Restores equipment using the employer sequence
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
The main purpose of LOTO is to:
2
Before servicing begins, the authorized employee must verify:
3
Who normally applies personal lockout devices for covered servicing?
4
Stored energy such as pressure or gravity must be:
5
A stop button is:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
Affected employees should be notified:
7
If conditions allow energy to reaccumulate, workers should:
8
Group LOTO should provide each authorized employee:
9
This downloadable course alone authorizes an employee to perform LOTO on any machine.
10
When outside servicing personnel perform covered work, host and contractor employers should:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize hazardous energy sources and when LOTO applies
02
Someone says “it is off” but cannot identify all energy sources
03
Show the written energy-control program and machine-specific procedures
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.147
Training use note
General/formal instruction. Employer- and machine-specific energy-control procedures are still required.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/laws-regs/regulations/standardnumber/1910/1910.147
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.