## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Order Picker / Stock Picker
Professional downloadable safety training
TRAINING OUTCOME
Recognize elevated-platform, fall and crushing hazards
AUDIENCE
Order-picker operators
TIME
30-40 min
REFERENCE
29 CFR 1910.178(l)
USE NOTE
Equipment-specific formal instruction. Practical training and workplace evaluation are required; fall protection must follow the truck/manufacturer and employer requirements.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Order Picker / Stock Picker to the actual work employees perform. Equipment-specific formal instruction. Practical training and workplace evaluation are required; fall protection must follow the truck/manufacturer and employer requirements.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
The operator goes up
Order pickers elevate the operator with the load platform, creating fall and overhead exposure.
Fall protection and body position
Use the manufacturer-required harness/restraint and approved anchorage.
Travel and elevation
Follow manufacturer/site rules for travel with the platform elevated.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize elevated-platform, fall and crushing hazards
02
Use required fall-restraint/fall-protection systems correctly
03
Control travel and platform elevation in narrow aisles
04
Pick/place loads without overreach or unstable body position
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
The operator goes up
Start with what the employee is exposed to.
Order pickers elevate the operator with the load platform, creating fall and overhead exposure.
The truck must be used only as designed, with required gates/rails and fall-protection systems.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - The operator goes up,Order pickers elevate the operator with the load platform, creating fall and overhead exposure.,The truck must be used only as designed, with required gates/rails and fall-protection systems.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Fall protection and body position
Tie every point to a visible action or decision.
Use the manufacturer-required harness/restraint and approved anchorage.
Keep gates/rails in position and do not climb on them.
Do not overreach; reposition the truck/platform.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Fall protection and body position,Use the manufacturer-required harness/restraint and approved anchorage.,Keep gates/rails in position and do not climb on them.,Do not overreach; reposition the truck/platform.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Travel and elevation
Tie every point to a visible action or decision.
Follow manufacturer/site rules for travel with the platform elevated.
Control speed and maintain clearance from rack beams, sprinklers and other overhead hazards.
Stop and lower when visibility or aisle conditions are not controlled.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Travel and elevation,Follow manufacturer/site rules for travel with the platform elevated.,Control speed and maintain clearance from rack beams, sprinklers and other overhead hazards.,Stop and lower when visibility or aisle conditions are not controlled.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Picking and load control
Tie every point to a visible action or decision.
Stay within platform capacity and keep picked product stable.
Secure loose items and keep platform floor clear.
Use proper ergonomics and avoid twisting from unstable positions.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Picking and load control,Stay within platform capacity and keep picked product stable.,Secure loose items and keep platform floor clear.,Use proper ergonomics and avoid twisting from unstable positions.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Pedestrians and aisles
Tie every point to a visible action or decision.
Control access below/around the elevated platform.
Use horns, lights, barriers or spotters as the site requires.
Never allow a person under elevated forks/platform components.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Pedestrians and aisles,Control access below/around the elevated platform.,Use horns, lights, barriers or spotters as the site requires.,Never allow a person under elevated forks/platform components.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Inspection and rescue readiness
Tie every point to a visible action or decision.
Inspect lift chains/mast, controls, gates, fall-protection equipment and anchorage.
Know emergency lowering/rescue procedures and who can respond.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Inspection and rescue readiness,Inspect lift chains/mast, controls, gates, fall-protection equipment and anchorage.,Know emergency lowering/rescue procedures and who can respond.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Harness/lanyard/restraint is not connected as required
02
Gate is open or bypassed while elevated
03
Operator overreaches outside the platform
04
Travel path has overhead obstructions or people below
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
An operator cannot reach a carton from the elevated platform without leaning past the guardrail. What should they do?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Stop, lower/reposition the truck or platform and maintain the required body position and fall-protection system; do not overreach.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Stop, lower/reposition the truck or platform and maintain the required body position and fall-protection system; do not overreach.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Manufacturer-required fall protection/restraint and anchorage
✓
Rules for elevated travel and aisle control
✓
Emergency lowering/rescue procedure
✓
Hands-on picking at height and workplace evaluation
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Inspects truck and fall-protection equipment
Connects restraint/harness correctly
Maintains gates/rails
Controls platform height/travel
Maintains overhead clearances
Uses safe reach/body position
Controls pedestrian exposure below
Demonstrates emergency lowering knowledge
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
The main difference with an order picker is that:
2
When required by the truck/manufacturer, the operator should use:
3
If an item is out of reach, the operator should:
4
People should be kept:
5
Overhead hazards can include:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
Platform floor should be:
7
Emergency lowering procedures should be:
8
Travel with the platform elevated should:
9
Fall-protection equipment should be inspected:
10
This course replaces practical training/evaluation.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize elevated-platform, fall and crushing hazards
02
Harness/lanyard/restraint is not connected as required
03
Manufacturer-required fall protection/restraint and anchorage
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.178(l)
Training use note
Equipment-specific formal instruction. Practical training and workplace evaluation are required; fall protection must follow the truck/manufacturer and employer requirements.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/etools/powered-industrial-trucks/workplace/narrow-aisles
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.