## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Scissor Lift Safety
Professional downloadable safety training
TRAINING OUTCOME
Recognize fall, tip-over, crushing, electrical and falling-object hazards
AUDIENCE
Scissor-lift users
TIME
30-40 min
REFERENCE
OSHA scissor lift guidance / applicable scaffold & training requirements
USE NOTE
General/formal instruction. The employer must provide equipment-specific training, manufacturer instructions and verify safe operation for the actual lift and workplace.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Scissor Lift Safety to the actual work employees perform. General/formal instruction. The employer must provide equipment-specific training, manufacturer instructions and verify safe operation for the actual lift and workplace.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Five major hazard groups
Falls from the platform.
Pre-use and work-area inspection
Inspect controls, emergency lowering, guardrails/gates, tires, leaks, alarms and safety devices.
Stable setup
Use only on surfaces and slopes permitted by the manufacturer.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize fall, tip-over, crushing, electrical and falling-object hazards
02
Complete a pre-use/work-area inspection
03
Position, elevate, travel and lower the lift safely
04
Apply manufacturer, site and weather/wind restrictions
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Five major hazard groups
Start with what the employee is exposed to.
Falls from the platform.
Tip-over/collapse from unstable setup, overload or environmental conditions.
Crushing/entrapment against overhead structures.
Electrical contact with energized conductors.
Falling objects striking people below.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Five major hazard groups,Falls from the platform.,Tip-over/collapse from unstable setup, overload or environmental conditions.,Crushing/entrapment against overhead structures.,Electrical contact with energized conductors.,Falling objects striking people below.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Pre-use and work-area inspection
Tie every point to a visible action or decision.
Inspect controls, emergency lowering, guardrails/gates, tires, leaks, alarms and safety devices.
Inspect the floor/ground for holes, drop-offs, slopes, debris and weak surfaces.
Identify overhead power, beams, piping and moving equipment.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Pre-use and work-area inspection,Inspect controls, emergency lowering, guardrails/gates, tires, leaks, alarms and safety devices.,Inspect the floor/ground for holes, drop-offs, slopes, debris and weak surfaces.,Identify overhead power, beams, piping and moving equipment.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Stable setup
Tie every point to a visible action or decision.
Use only on surfaces and slopes permitted by the manufacturer.
Do not exceed platform capacity or use makeshift devices to gain height.
Do not move the lift in a way prohibited by the manufacturer when elevated.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Stable setup,Use only on surfaces and slopes permitted by the manufacturer.,Do not exceed platform capacity or use makeshift devices to gain height.,Do not move the lift in a way prohibited by the manufacturer when elevated.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Falls and body position
Tie every point to a visible action or decision.
Keep gates/rails in place and maintain firm footing on the platform.
Do not climb or stand on guardrails.
Use fall protection only as required by applicable rules, manufacturer instructions and employer program; use approved anchorage only.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Falls and body position,Keep gates/rails in place and maintain firm footing on the platform.,Do not climb or stand on guardrails.,Use fall protection only as required by applicable rules, manufacturer instructions and employer program; use approved anchorage only.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Crushing and electrical
Tie every point to a visible action or decision.
Keep adequate clearance from overhead structures and energized lines.
Use a spotter/ground guide where visibility is limited.
Move slowly in congested areas and avoid trapping the operator between platform controls and structure.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Crushing and electrical,Keep adequate clearance from overhead structures and energized lines.,Use a spotter/ground guide where visibility is limited.,Move slowly in congested areas and avoid trapping the operator between platform controls and structure.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Weather and emergency response
Tie every point to a visible action or decision.
Follow manufacturer wind limits and remove the lift from service in unsafe weather.
Know emergency stop/lowering procedures.
Keep the area below controlled when falling objects are possible.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Weather and emergency response,Follow manufacturer wind limits and remove the lift from service in unsafe weather.,Know emergency stop/lowering procedures.,Keep the area below controlled when falling objects are possible.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Guardrail/gate or control is damaged
02
Lift is on an unapproved slope or unstable surface
03
Wind/environmental conditions exceed manufacturer limits
04
Operator is climbing on rails or working close to power/overhead structure without clearance
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A scissor lift is fully elevated outdoors and wind begins gusting strongly. The operator is below the manufacturer’s rated platform capacity. What should happen?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Capacity alone does not make the situation safe. Follow the manufacturer wind limit and employer procedure; lower and discontinue use if conditions are outside safe limits.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Capacity alone does not make the situation safe. Follow the manufacturer wind limit and employer procedure; lower and discontinue use if conditions are outside safe limits.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Actual lift model, controls, emergency lowering and manufacturer limits
✓
Indoor/outdoor surface and wind rules
✓
Electrical clearance and overhead-crush controls
✓
Site traffic/pedestrian barricades and rescue response
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Performs pre-use inspection
Inspects floor/ground and overhead area
Uses gate/guardrails correctly
Maintains safe body position
Controls travel/elevation smoothly
Maintains overhead/electrical clearance
Applies site barricade/spotter rules
Demonstrates emergency stop/lowering
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
A scissor lift can tip because of:
2
The platform guardrails are intended to:
3
Before elevating, the operator should inspect:
4
Standing on the guardrail to gain extra height is:
5
Wind limits should come from:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
Overhead crushing hazards require:
7
Electrical hazards should be controlled by:
8
People below the lift should:
9
Emergency lowering controls should be:
10
This course alone qualifies an employee on every scissor-lift model.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize fall, tip-over, crushing, electrical and falling-object hazards
02
Guardrail/gate or control is damaged
03
Actual lift model, controls, emergency lowering and manufacturer limits
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
OSHA scissor lift guidance / applicable scaffold & training requirements
Training use note
General/formal instruction. The employer must provide equipment-specific training, manufacturer instructions and verify safe operation for the actual lift and workplace.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/etools/scaffolding/scissor-lifts/
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.