## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Sit-Down Counterbalance Forklift
Professional downloadable safety training
TRAINING OUTCOME
Recognize counterbalance truck stability and rear-swing hazards
AUDIENCE
Sit-down counterbalance operators
TIME
30-40 min
REFERENCE
29 CFR 1910.178(l)
USE NOTE
Equipment-specific formal instruction. Hands-on training and workplace evaluation on the actual truck type are required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Sit-Down Counterbalance Forklift to the actual work employees perform. Equipment-specific formal instruction. Hands-on training and workplace evaluation on the actual truck type are required.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Counterbalance geometry
The counterweight balances the load across the front axle pivot.
Mounting and operator restraint
Use three points of contact where applicable.
Travel position and steering
Carry the load low and tilted only enough for stability.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize counterbalance truck stability and rear-swing hazards
02
Use correct mounting, restraint, travel and load-handling practices
03
Inspect the truck and respond to defects
04
Demonstrate safe turning, stacking, parking and dock approach
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Counterbalance geometry
Start with what the employee is exposed to.
The counterweight balances the load across the front axle pivot.
Turning, speed, slopes, load height and off-center loads can move the combined center of gravity outside the stability area.
Rear steering creates tail swing.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Counterbalance geometry,The counterweight balances the load across the front axle pivot.,Turning, speed, slopes, load height and off-center loads can move the combined center of gravity outside the stability area.,Rear steering creates tail swing.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Mounting and operator restraint
Tie every point to a visible action or decision.
Use three points of contact where applicable.
Use the operator restraint/seat belt provided by the manufacturer.
Keep body parts inside the operator compartment and never jump from a tipping sit-down truck.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Mounting and operator restraint,Use three points of contact where applicable.,Use the operator restraint/seat belt provided by the manufacturer.,Keep body parts inside the operator compartment and never jump from a tipping sit-down truck.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Travel position and steering
Tie every point to a visible action or decision.
Carry the load low and tilted only enough for stability.
Turn smoothly and slow before corners.
Watch rear swing near racks, people, columns and doorways.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Travel position and steering,Carry the load low and tilted only enough for stability.,Turn smoothly and slow before corners.,Watch rear swing near racks, people, columns and doorways.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
Load pickup and placement
Tie every point to a visible action or decision.
Square to the load, level forks, enter fully and center the load.
Check load stability and capacity before lifting.
Raise only when stopped and positioned for stacking.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - Load pickup and placement,Square to the load, level forks, enter fully and center the load.,Check load stability and capacity before lifting.,Raise only when stopped and positioned for stacking.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Ramps, docks and trailers
Tie every point to a visible action or decision.
Follow site rules for direction of travel on grades with loads.
Keep clear of dock edges and verify dock plates and trailer restraint.
Account for wet surfaces, debris and limited clearances.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Ramps, docks and trailers,Follow site rules for direction of travel on grades with loads.,Keep clear of dock edges and verify dock plates and trailer restraint.,Account for wet surfaces, debris and limited clearances.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Shutdown and parking
Tie every point to a visible action or decision.
Lower forks fully, neutralize controls, set brake and shut off power when unattended.
Park only in approved areas without blocking exits, aisles or emergency equipment.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Shutdown and parking,Lower forks fully, neutralize controls, set brake and shut off power when unattended.,Park only in approved areas without blocking exits, aisles or emergency equipment.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Seat belt/restraint is damaged or bypassed
02
Turning fast with a raised load
03
Operating close to rack uprights without accounting for tail swing
04
Entering a trailer without confirmed restraint/chocks and floor condition
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A sit-down forklift begins to tip sideways during a turn. What should the seated operator do?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Stay in the operator compartment, hold on, brace and lean away from the direction of the tip; do not jump from a tipping sit-down counterbalance truck.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Stay in the operator compartment, hold on, brace and lean away from the direction of the tip; do not jump from a tipping sit-down counterbalance truck.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Actual truck controls, capacity plate and attachments
✓
Site traffic plan, pedestrian routes and speed expectations
✓
Grade/ramp rules and dock/trailer procedures
✓
Hands-on stacking/unstacking and workplace evaluation
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Performs pre-use inspection
Mounts/dismounts safely
Uses seat belt/restraint
Controls speed and tail swing
Maintains correct travel/load position
Stacks and retrieves load smoothly
Uses safe dock/trailer procedure
Parks correctly
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
Rear-wheel steering means the operator must watch for:
2
A loaded counterbalance forklift should normally travel with the load:
3
During a tip-over in a seated sit-down forklift, the operator should generally:
4
Before lifting a load, the operator should check:
5
Fast turns increase:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
When parking unattended, forks should be:
7
A dock plate should be entered only after:
8
An attachment can:
9
Tail swing is most important near:
10
This course replaces practical evaluation on the actual truck.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize counterbalance truck stability and rear-swing hazards
02
Seat belt/restraint is damaged or bypassed
03
Actual truck controls, capacity plate and attachments
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.178(l)
Training use note
Equipment-specific formal instruction. Hands-on training and workplace evaluation on the actual truck type are required.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/etools/powered-industrial-trucks/training
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.