## Slide 1
TRAVISTILLEY.COM / TRAINING CENTER
Stand-Up Reach Truck
Professional downloadable safety training
TRAINING OUTCOME
Recognize narrow-aisle and stand-up operator hazards
AUDIENCE
Reach-truck operators
TIME
30-40 min
REFERENCE
29 CFR 1910.178(l)
USE NOTE
Equipment-specific formal instruction. Practical training and workplace evaluation on the reach truck are required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
1 / 17
Notes: Opening: Connect Stand-Up Reach Truck to the actual work employees perform. Equipment-specific formal instruction. Practical training and workplace evaluation on the reach truck are required.

## Slide 2
WHY THIS MATTERS
Start with the hazard. Build the safe decision.
Use this slide to connect the topic to what employees actually see, touch, drive or do.
Reach-truck differences
Narrow-aisle design changes visibility, steering feel and clearance needs.
Operator position
Stay within the protected operator compartment.
Narrow-aisle travel
Control speed before entering turns and cross aisles.
ASK THE ROOM
01
Where could this go wrong here?
02
What control keeps us safe?
03
What should make us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
2 / 17
Notes: Ask employees for examples from their own work area. Capture site-specific examples for later slides.

## Slide 3
LEARNING OBJECTIVES
What employees should be able to do
Keep the session practical: recognize the hazard, choose the control, know when to stop.
01
Recognize narrow-aisle and stand-up operator hazards
02
Control travel, turning and load placement at height
03
Use correct stance, body positioning and visibility practices
04
Inspect and operate reach mechanisms safely
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
3 / 17
Notes: Read each objective and identify which objective will need workplace-specific demonstration or examples.

## Slide 4
MODULE 1 / 6
Reach-truck differences
Start with what the employee is exposed to.
Narrow-aisle design changes visibility, steering feel and clearance needs.
Stand-up operator position creates different egress and impact hazards.
Reach mechanisms and high stacking require precise load control.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
4 / 17
Notes: Trainer notes - Reach-truck differences,Narrow-aisle design changes visibility, steering feel and clearance needs.,Stand-up operator position creates different egress and impact hazards.,Reach mechanisms and high stacking require precise load control.,Ask for one real workplace example and one stop-work trigger.

## Slide 5
MODULE 2 / 6
Operator position
Tie every point to a visible action or decision.
Stay within the protected operator compartment.
Keep feet and body parts inside the truck profile.
Use the manufacturer-prescribed stance and controls.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
5 / 17
Notes: Trainer notes - Operator position,Stay within the protected operator compartment.,Keep feet and body parts inside the truck profile.,Use the manufacturer-prescribed stance and controls.,Ask for one real workplace example and one stop-work trigger.

## Slide 6
MODULE 3 / 6
Narrow-aisle travel
Tie every point to a visible action or decision.
Control speed before entering turns and cross aisles.
Account for rack uprights, end-of-aisle traffic and pedestrians.
Travel in the direction that provides best safe visibility based on truck design and site rules.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
6 / 17
Notes: Trainer notes - Narrow-aisle travel,Control speed before entering turns and cross aisles.,Account for rack uprights, end-of-aisle traffic and pedestrians.,Travel in the direction that provides best safe visibility based on truck design and site rules.,Ask for one real workplace example and one stop-work trigger.

## Slide 7
MODULE 4 / 6
High stacking
Tie every point to a visible action or decision.
Square to the rack before raising.
Verify rack capacity/condition and pallet integrity.
Raise while stopped; use reach/tilt smoothly and watch overhead clearance.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
7 / 17
Notes: Trainer notes - High stacking,Square to the rack before raising.,Verify rack capacity/condition and pallet integrity.,Raise while stopped; use reach/tilt smoothly and watch overhead clearance.,Ask for one real workplace example and one stop-work trigger.

## Slide 8
MODULE 5 / 6
Stability and loads
Tie every point to a visible action or decision.
Know capacity at lift height and load center.
Avoid sudden steering, braking or mast movement with elevated loads.
Do not travel with the load unnecessarily elevated.
FIELD DECISION
01
Where could this fail?
02
What control do we use?
03
What makes us stop?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
8 / 17
Notes: Trainer notes - Stability and loads,Know capacity at lift height and load center.,Avoid sudden steering, braking or mast movement with elevated loads.,Do not travel with the load unnecessarily elevated.,Ask for one real workplace example and one stop-work trigger.

## Slide 9
MODULE 6 / 6
Inspection and defects
Tie every point to a visible action or decision.
Inspect forks, mast, reach mechanism, chains, wheels, controls, battery, horn and safety systems.
Remove the truck from service for conditions that affect safe operation.
FIELD DECISION
01
What changes the risk?
02
What must the employee do?
03
Who needs to know?
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
9 / 17
Notes: Trainer notes - Inspection and defects,Inspect forks, mast, reach mechanism, chains, wheels, controls, battery, horn and safety systems.,Remove the truck from service for conditions that affect safe operation.,Ask for one real workplace example and one stop-work trigger.

## Slide 10
STOP-WORK / RED-FLAG CONDITIONS
These are the moments to slow down and regain control.
01
Foot or leg extends outside the operator compartment
02
Traveling with elevated load in a narrow aisle
03
Racking is visibly damaged or pallet integrity is questionable
04
Operator loses clear view of pedestrians at aisle ends
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
10 / 17
Notes: Ask which red flag is easiest to miss during a busy shift. Reinforce the site stop-work/escalation process.

## Slide 11
SCENARIO DISCUSSION
What would you do next?
Give the group 30-60 seconds before revealing the recommended response.
A reach-truck operator has a pallet raised near the top rack and needs to reposition the truck sideways. What is the safe approach?
DISCUSS
01
What is the hazard?
02
What control is missing?
03
What is the safest next action?
04
What is our site rule?
RECOMMENDED RESPONSE
Lower the load to a stable travel position before repositioning unless the manufacturer/site procedure specifically allows a controlled adjustment at height; avoid traveling with a high load.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
11 / 17
Notes: Recommended response: Lower the load to a stable travel position before repositioning unless the manufacturer/site procedure specifically allows a controlled adjustment at height; avoid traveling with a high load.,Ask employees to name the site-specific action and who they would contact.

## Slide 12
SITE-SPECIFIC APPLICATION
This is where generic training becomes your program.
Replace examples with your actual equipment, procedures, hazards and expectations.
✓
Truck-specific controls and emergency features
✓
Aisle widths, intersections, speed limits and pedestrian controls
✓
Rack inspection/damage reporting and pallet standards
✓
Hands-on high stacking and workplace evaluation
BEFORE WORK
01
Show the actual procedure
02
Show the actual equipment/task
03
Confirm questions are answered
04
Complete required evaluation
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
12 / 17
Notes: Use this slide to bridge classroom instruction to employer-specific training and verification.

## Slide 13
PRACTICAL / WORKPLACE VERIFICATION
Can the employee apply it?
Written knowledge matters. Safe performance in the real workplace matters more.
Inspects reach mechanism and safety systems
Maintains body position inside compartment
Controls speed in narrow aisles
Squares to racks before lifting
Uses reach/tilt smoothly
Places/retrieves load without rack contact
Maintains safe travel height
Parks/charges safely
Use the included evaluation form when hands-on demonstration or workplace verification is appropriate or required.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
13 / 17
Notes: Explain who is qualified/authorized to evaluate this at your company and what constitutes acceptable performance.

## Slide 14
KNOWLEDGE CHECK / PART 1
Knowledge check 1-5
Use the printable test in the course package for employee responses.
1
A stand-up reach truck operator should keep body parts:
2
High stacking should be done with the truck:
3
Traveling with a high elevated load:
4
Before placing a pallet high in racking, verify:
5
A narrow aisle requires extra attention to:
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
14 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 15
KNOWLEDGE CHECK / PART 2
Knowledge check 6-10
Use the printable test in the course package for employee responses.
6
Reach mechanism defects should result in:
7
Sudden steering with an elevated load:
8
Operator stance should follow:
9
Rack damage should be:
10
This course alone authorizes reach-truck operation.
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
15 / 17
Notes: Do not coach answers while employees are testing. Review missed items afterward and document any retraining needed.

## Slide 16
TAKE IT BACK TO THE FLOOR
Know the hazard. Use the control. Stop when it is not right.
01
Recognize narrow-aisle and stand-up operator hazards
02
Foot or leg extends outside the operator compartment
03
Truck-specific controls and emergency features
NEXT STEPS
01
Answer questions
02
Complete site-specific training
03
Complete required hands-on evaluation
04
Document attendance/completion
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
16 / 17
Notes: Close by asking for questions. Confirm what site-specific training/evaluation remains before employees perform the task independently.

## Slide 17
REFERENCE / USE NOTE
Use this package as a strong training foundation.
Always align the material to current requirements, manufacturer instructions and your own procedures.
Primary reference
29 CFR 1910.178(l)
Training use note
Equipment-specific formal instruction. Practical training and workplace evaluation on the reach truck are required.
BEFORE YOU DELIVER
✓
Confirm current OSHA/state-plan requirements
✓
Insert your procedures and equipment information
✓
Use qualified/competent trainers where required
✓
Complete practical/workplace evaluation where required
✓
Keep training and authorization records
https://www.osha.gov/etools/powered-industrial-trucks/workplace/narrow-aisles
TRAVISTILLEY.COM / PROFESSIONAL SAFETY TRAINING
17 / 17
Notes: Reference slide. Confirm the source before delivery and update site-specific content.